Objective

To use a geocoding tool to learn how to quickly georeference addresses and place address points on a map.

Data

counties.shp, addresses_for_geocoding.xls

The GIS Project

- Open the addresses_for_geocoding spreadsheet, which contains address we would like to see mapped. These have been parsed into street address, city, state and zip already, but you may have to manually do this is the future.

- Open ArcMap. Choose to start with a blank map.

- Add Data (). Browse to the s2-geocoding folder and choose to add the addresses_for_geocoding.xls spreadsheet. Add Sheet1$.

- We are now going to geocode the addresses contained in the table, which means to assign latitude and longitude to address data. Right click on Sheet1$ and choose Geocode Addresses.

- You will see that there are several built in Address Locators that you can access as long you are connected to the internet. Choose the 10.0 US Streets Geocode Service (ArcGIS Online).

- You will see that since our table is named nicely, the geocoding service can recognize which fields we want to use. Make sure your output dataset is named something appropriate (NOT geocoding_result.shp).

- Click Geocoding Options. Set Minumum Match Score to 100. We only want the geocoder to match addresses that it is 100% confident in. Also check the boxes for X and Y Coordinates and Standardized Addresses.

- Click Ok twice to run the geocoder. It will give you the results. Click Close.

- New points are added to your map. Open up the Attribute Table for the new points. We can see that we have three unmatched records.

- Add the Geocoding Toolbar by clicking on Customize > Toolbars >Geocoding.

- Click the  button on your new toolbar to rematch your unmatched addresses. On the interactive rematch screen you can go through your addresses one by one and choose from lists of candidate addresses. Match all three of your unmatched addresses.

- For VOA Site C RD, you will have to manually type spaces in between the VOA initials and hit enter. Misspellings such as this will often prevent candidates from popping up.

- Once all your points are matched, add the counties layer, and map elements to create a finished layout.