Prenatal Screening for Group B Streptococcus

(Non-pigmented broth, plate subculture only for isolation and identification)

Annual Review:

| Name/Title | Signature | Date |
| --- | --- | --- |

Revision History:

| Revision # | Control # | Changes made to document section | Author | Date |
| --- | --- | --- | --- | --- |

Approval Signatures:

Approved by: 	_______________________________	Date: 	__________________

Author

____________________________________________________________

Print Name and Title

Approved by: 	_______________________________	Date: 	__________________

Supervisor/Technical Specialist-Director																			____________________________________________________________

Print Name and Title

Approved by: 	_______________________________	Date: 	__________________

Quality Manager

____________________________________________________________

Print Name and Title

Purpose/Principle:

The purpose of this document is to provide instructions for performing prenatal screening for Group B Streptococcus from appropriately collected vaginal/rectal specimens using enriched non-pigmented broth followed by plate culture.

Scope:

This document applies to laboratory assistants, technicians and technologists within the Division of Microbiology at XXXX.

Related documents:

- Provider collection procedure for Prenatal Screening for Group B Streptococcus - # xxxx.  Note: Procedure should specify the acceptable specimen is a vaginal-rectal swab and that swabs from other sites (e.g. cervical or perianal swabs only) are not acceptable. Procedure should list acceptable type of swab and transport medium.

- Quality Control procedure for tube and plated media - # xxxx.

- Procedure for the identification of streptococci - # xxxx.

- Notification procedure for positive Prenatal Screening for Group B Streptococcus - # xxxx.

- Procedure for susceptibility testing of Group B Streptococcus - # xxxx.

Responsibility:

- It is the responsibility of the technical staff of the microbiology laboratory to review and assure they are familiar with the processes outlined in this document which are within their job duties.

- It is the responsibility of the technical specialist to keep this procedure updated and current with national standards/guidelines/recommendations.

- It is the responsibility of the microbiology supervisor to accurately train and assess the competency of all microbiology staff involved in performing this procedure.

- It is the responsibility of the microbiology data technologist to assure that reporting of all results is appropriate in all computer systems.

- It is the responsibility of the technical director to approve this procedure on an annual basis.

Definitions:

N/A

Equipment/Materials:

- Trans-Vag broth supplemented with 5% defibrinated sheep blood, LIM broth (or equivalent)

#### Agar plates for subculture (available from a variety of manufacturers): Sheep blood agar, neomycin-nalidixic acid (NNA) agar, Columbia colistin and naladixic acid (CNA) agar with 5% sheep blood, or other selective Streptococcus agar; GBS Detect™ agar (Hardy Diagnostics, Santa Maria, CA); CHROMagar™ StrepB (distributed by Gibson Laboratories, LLC, Lexington, KY), ChromID Strepto B agar (bioMérieux, Inc., Durham, NC), or other chromogenic medium designed for detection of Group B Streptococcus, including non-ß-hemolytic strains.

3.  Sterile loops

4.  Incinerator

5.  Incubator

Quality Control:

Follow Quality Control procedures for tube and plated media - # xxxx.

Safety Precautions:

Use standard precautions when performing this procedure.

Procedure: (Appendix includes one-page flowchart)

- Remove patient specimen (swab; swabs) from transport medium. Specimens should be processed within 4 days of collection.  Specimens requiring more than 24 hr of transport time should be refrigerated until received and processed by the laboratory.

- Inoculate swab(s) into a recommended selective enrichment broth medium, such asTrans-Vag broth supplemented with 5% defibrinated sheep blood, LIM broth or equivalent. [Before inoculating into broth, laboratories may choose to direct plate by rolling the swab(s) on a sheep blood agar plate, NNA agar, CNA agar, other selective Streptococcus agar. If Group B Streptococcus is identified from the primary plate, report Group B streptococcus positive on the culture report.  If Group B Streptococcus is not identified from the primary plate, plate should be discarded, and enriched broth processed as per protocol below and results reported out from enriched broth].

- Incubate inoculated selective broth for a minimum of 18-24 hours at 35-37oC in ambient air or 5% CO2 as recommended by the manufacturer.  The broth should display visible turbidity as an indicator of adequate specimen collection. A clear broth after 24 hours of incubation indicates failure to obtain a proper sample and a new specimen should be requested.

- Subculture the incubated broth to a sheep blood agar plate, NNA agar, CNA agar, other selective Streptococcus agar; GBS Detect™ agar, or chromogenic medium such as CHROMagar™ StrepB, ChromID Strepto B agar that will detect non-hemolytic Group B Streptococcus and incubate a minimum of  18-24 hour at 35-37oC in 5% CO2 or as recommended by the manufacturer.

- Inspect and identify colonies characteristic of Group B Streptococcus (i.e., gram-positive cocci, catalase negative, narrow zone of -hemolysis or no hemolysis) using routine laboratory identification protocols. (Refer to procedure # xxxx – Procedure for the identification of streptococci).

- If Group B Streptococcus is not identified, reincubate the agar plate for an additional overnight incubation to identify suspected Group B Streptococcus organisms.

- Report as negative for Group B Streptococcus when no Group B Streptococcus has been recovered.

- If Group B Streptococcus is identified, report Group B streptococcus positive on the culture report.

- If the positive specimen is from a penicillin-allergic patient at high risk for anaphylaxis, perform susceptibilities for clindamycin and erythromycin, including inducible clindamycin resistance, using appropriate laboratory susceptibility procedures. (Refer to protocol # xxxx – Procedure for susceptibility testing of Group B Streptococcus.)

Format:

N/A

Reference:

MMWR Recomm Rep. 2010 Nov 19;59(RR-10):1-36.  Prevention of perinatal group B streptococcal disease--revised guidelines from CDC, 2010.  Verani JR, McGee L, Schrag SJ; Division of Bacterial Diseases, National Center for Immunization and Respiratory Diseases, Centers for Disease Control and Prevention (CDC).

Appendix:  Flow diagram for Prenatal Screening for Group B Streptococcus: Non-pigmented broth, plate subculture only for isolation and identification.

# Text boxes

Experts from the American Society for Microbiology (ASM) and the  Centers for Disease Control and Prevention’s (CDC) Streptococcus Laboratory co-authored this document.*

For more GBS laboratory resources, visit http://www.cdc.gov/groupbstrep

*Collaboration does not imply HHS/CDC endorsement of ASM